CAB-00042 – Wired Motor – Orbita
Ver.	Date	Pub	Chk	Description
A1	24/01/2023	EB	AC	Initial drawing.
B1	27/03/2023	EB	AC	Now using Hall sensors

Description
24V BLDC Motor (+Reduction + Encoder) wired for Orbita.
Bill of Material
Item	Description	L (mm)	Qtté	Ref. Farnell / RS
BLDC Motor 24V + Reductor + Encoder	ECXTQ22M+GPX22R1C+ENX22		1	Provided par Pollen
Molex PicoBlade Fem. Housing 5 ways	51021-0500		1	/
Contacts for PicoBlade	50079-8000		5	/
Molex MicroFit Fem. Housing 3 ways	43645-0300		1	/
Contacts for MicroFit	46235-0001		3	2284551 /
Gaine thermo

Assembly
Molex PicoBlade Contacts are crimped with the Molex 63811-0000 Tool.
Molex MicroFit Contacts are crimped with the Molex 64016-0201 Tool.
1. Drawing
2. Nota
Please note that the wires 1-brown and 2-black must be taken from the 10-way connector pin #2 and #3.