CAB-00043 – Reachy-Orbita-Head-Supply Cable
Ver.	Date	Pub	Chk	Description
A1	14/02/2023	EB	AC	Initial drawing.

Description
Delivering 12V from PCB Major Tom to DXL-Fan-Luos Module in order to supply the antenna’s motors. Please note that this cable goes through Orbita and thus requires to be made directly on Orbita.
Bill of Material
Item	Description	L (mm)	Qtté	Ref. Farnell / RS
Wire	0,3 mm²	350	2
Hirose DF11 Fem. Housing 8 ways	DF11-8DS-2C		1	1688304 /
MicroFit Fem. Housing 2 ways	43645-0200		1	3076015 /
Contacts for DF11	DF11-2428SC		2	1688393 /
Contacts for MicroFit	46235-0001		2	2284551 /
Prolongateur	22AWG - 16AWG		2	587321 /

Assembly
Hirose DF11 Contacts are crimped with Hirose HT801/DF11-2428S(A) Tool
Molex MicroFit Contacts are crimped with the Molex 64016-0201 Tool.
Drawing

Nota
Again, note that this cable requires to be made directly on Orbita.